## Slide 1: DRIFT: Distributed Real-time Inertial and Frame Tracking on Resource-Constrained ESP32 Hardware
Phillipp Gery, Vedant Patkar, Francisco Benitez, Jack Kester and Sam Pisciotta

## Slide 2: Localization Without GPS, Without a Real Computer
Indoor, underground, GPS-denied → robots need self contained pose estimation
State-of-the-art VIO (ORB-SLAM3, VINS-Mono) targets ARM Cortex-A / GPU
We target a ESP32-S3 — two orders of magnitude less compute
Why care? Inspection swarms, search-and-rescue, indoor wearables — all deploy at MCU scale

## Slide 3: Hardware Constrains
Scale ambiguity: monocular vision can't recover metric scale alone
Compute wall: SVD, Essential matrices, RANSAC don't fit a 240 MHz dual core
Drift wall: MEMS gyro bias is the silent killer — drift is quadratic in time
Pure IMU dead-reckoning fails after a few seconds; pure vision fails on scale

## Slide 4: Hardware Constrains
Scale ambiguity: monocular vision can't recover metric scale alone
Compute wall: SVD, Essential matrices, RANSAC don't fit a 240 MHz dual core
Drift wall: MEMS gyro bias is the silent killer — drift is quadratic in time
Pure IMU dead-reckoning fails after a few seconds; pure vision fails on scale

## Slide 5: System Architecture

## Slide 6: Experimental Setup
Four Different nodes:
    Node 1 — WE ISDS + VIO. Industrial-grade Würth
    Node 2 — MPU-6050 + VIO. Hobby-grade
    Node 3 — WE ISDS only. IMU dead-reckoning.
    Node 4 — MPU-6050 only. IMU dead-reckoning.
Five Scenarios:
    Static, 10 s / Straight line, 2 m / Rectangle, 1.0 m ×0.5 m / Circle, 40 cm diameter / Free-form path

## Slide 7: Results

## Slide 8: Hardware Constrains
Scale ambiguity: monocular vision can't recover metric scale alone
Compute wall: SVD, Essential matrices, RANSAC don't fit a 240 MHz dual core
Drift wall: MEMS gyro bias is the silent killer — drift is quadratic in time
Pure IMU dead-reckoning fails after a few seconds; pure vision fails on scale

## Slide 9: Conclusion and Future Steps
Done:
  ✓ End-to-end VIO on bare-metal ESP32-S3
  ✓ IPM + gyro derotation + planar EKF
  ✓ Drift bounded on closed-loop trajectories where IMU-only diverges
Future Steps:
  TinyML motion-class auxiliary channel (Edge Impulse) for adaptive filter tuning

## Slide 10: Thank You